## Slide 1: Car driver drowsiness detection
Federico Cavedoni
Francesco Bruno

## Slide 2: Drowsiness detection system
A system capable of understanding if the
driver is falling asleep by analysing his hearthbeat

## Slide 3: System description
The system is composed of:
ECG Sensor (Polar T34)
Sensor Controller (Raspberry PI 3)
Classification Server

## Slide 4: prototype description (1/2)
Hardware description
Polar T34
Raspberry PI 3
Polar Heart Rate Receiver

## Slide 5: prototype description (2/2)
Classifier Server Software
• Communication_API.py
• Controller_firmware.py
• Hearth_beat_analysis.py
• Sensor_driver.py
• Communication_API.py
• Project_network.py
• Thread_receiver.py
Controller Software

## Slide 6: Performance evaluation (1/3)
KNeighborsClassifier
KNeighborsClassifier is used because it has great accuracy and good precision, respect to other types of classifiers
Scheduling
Scheduling is managed by the Raspbian O.S.

## Slide 7: Performance evaluation (2/3)
Our SamplingTask is: (Soft – Firm – Hard) Real Time?
Firm-Task, because with deadline miss, it will lose the data becoming useless for the system. This event has been handled invalidating the session, restarting the sampling session (60s).
Periodic ?
Aperiodic ?
Sporadic ?
Minumum Interrival Time ~ 272mS
220BPM

## Slide 8: Performance evaluation (3/3)
Deadline Analysis
Sampling session: ~4 hours Minimum Interarrival Time: ~272mS
WCET taskISR: ~510uS
WCET MainThread: ~140mS

## Slide 9: Demo (1/3): Normal situation

## Slide 10: Demo (2/3): Abnormal classification

## Slide 11: Demo (3/3): hands off steering wheel

## Slide 12: conclusions
Improve the training procedure
The classification is surely influenced by the unbalanced dataset used
Use a PPG sensor
For better classification due to the incrementing of the sensor precision and usability

## Slide 13: references
PPG Cognitive Fatigue Prediction Source: https://www.kaggle.com/code/katariinaparkja/ppg-cognitive-fatigue-prediction

## Slide 14: Thanks for the attention
Federico Cavedoni
Francesco Bruno